## Slide 1: I2C backplane specification
https://github.com/araobp

## Slide 2: Specification
Master-slave I2C backplane
Max seven I2C slaves supported
Plug&play with I2C general call

## Slide 3: I2C backplane
Master
Slave
0x10
Slave
0x11
Slave
0x12
Slave
0x16
…
Max seven slaves
Vdd
3k ohm
3k ohm
Mini PLC
UART
I2C

## Slide 4: Slave start sequence
Start
Initialize device
Wait PLG
Mode?
I2C mode
setup
UART mode
setup
Enable PLG general call
PLG (general call) received
2sec timeout

## Slide 5: Scheduler and 100msec time slot
#0 | PLG
#1 | CMD
#2 | (SEN)
#3 | (SEN)
#4 | (SEN)
#5 | (SEN)
#6 | CMD
#7 | (SEN)
#8 | (SEN)
#9 | (SEN)
current slot
Slave 0x12
Slave 0x11
Slave 0x10
100 msec
General call
Master

## Slide 6: Slave with two MSSPs enabled
Slave
I2C write “SEN”
Master
I2C read
Another I2C device
I2C
MSSP2
(I2C master)
MSSP1
(I2C slave)

## Slide 7: Command from UART
#0 | PLG
#1 | CMD
#2 | (SEN)
#3 | (SEN)
#4 | (SEN)
#5 | (SEN)
#6 | CMD
#7 | (SEN)
#8 | (SEN)
#9 | (SEN)
current slot
100 msec
Command queue
UART

## Slide 8: Caveats
I2C communications limited to one byte data at each time  to be improved