## Slide 1: I2C backplane specification
https://github.com/araobp

## Slide 2: Specification
Master-slave I2C backplane
Max seven I2C slaves supported
Plug&play with I2C general call

## Slide 3: I2C backplane
Master
Slave
0x10
Slave
0x11
Slave
0x12
Slave
0x16
…
Max seven slaves
Vdd
1~5k ohm
1~5k ohm
Mini PLC
UART
I2C
Interval: 50msec * scaler
(default scaler value: 1)

## Slide 4: Scheduler
Time-slot-based
Reduces the power supplied via I2C bus
Recommendation
Use MCU (such as PIC16F1) or mbed as a basis of mini PLC.
Linux is not good at real-time processing, so this I2C backplane may not work well.

## Slide 5: Scheduler and 50msec time slot
0 | PLG
1 | ACP
2 | CMD
3 | INV
4 | SEN
5 | INV
6 | SEN
7 | INV
8 | SEN
9 | ADT
10 | ACP
11 | CMD
12 | INV
13 | SEN
14 | INV
15 | SEN
16 | INV
17 | SEN
18 | INV
19 | SEN
Slave 0x12
Slave 0x11
Slave 0x10
50 msec
PLG General call
Master
CMD
INV
SEN
INV
SEN
INV
SEN
1sec
“*” (ACP)
<command>
IoT gateway

## Slide 6: Slave with two MSSPs enabled
Slave
I2C write “INV”
Master
Another I2C device
I2C
MSSP2
(I2C master)
MSSP1
(I2C slave)
I2C write “SEN”
I2C read (Type)
I2C read (Length)
I2C read (Value #0~#n)
50msec time slot 3a
50msec time slot 3b
:

## Slide 7: Command from UART
Buffer
Command
0 | PLG
1 | ACP
2 | CMD
3 | INV
4 | SEN
5 | INV
6 | SEN
7 | INV
8 | SEN
9 | ADT
10 | ACP
11 | CMD
12 | INV
13 | SEN
14 | INV
15 | SEN
16 | INV
17 | SEN
18 | INV
19 | SEN
Command
Command
Device
Device

## Slide 8: Extended-command redirection to I2C backplane
Slave
Master
I2C write “EXT”
I2C write (Length)
I2C write (Value #0~#n)
50msec time slot 3b
Extended command