## Slide 1: I2C backplane specification
https://github.com/araobp

## Slide 2: Specification
Master-slave I2C backplane
Max seven I2C slaves supported
Plug&play with I2C general call

## Slide 3: I2C backplane
Master
Slave
0x10
Slave
0x11
Slave
0x12
Slave
0x16
…
Max seven slaves
Vdd
3k ohm
3k ohm
Mini PLC
UART
I2C

## Slide 4: Slave start sequence
Start
Initialize device
Wait PLG
Mode?
I2C mode
setup
UART mode
setup
Enable PLG general call
PLG (general call) received
2sec timeout

## Slide 5: Scheduler and 50msec time slot
#0 | PLG
#1 | ADT
#2 | CMD
#3a | INV
#3b | SEN
#4a | INV
#4b | SEN
#5a | INV
#5b | SEN
#6a | INV
#6b | SEN
#7 | CMD
#8a | INV
#8b | SEN
#9a | INV
#9b | SEN
#10a | INV
#10b | SEN
#11a | INV
#11b | SEN
Slave 0x12
Slave 0x11
Slave 0x10
50 msec
General call
Master

## Slide 6: Slave with two MSSPs enabled
Slave
I2C write “INV”
Master
Another I2C device
I2C
MSSP2
(I2C master)
MSSP1
(I2C slave)
I2C write “SEN”
I2C read (Type)
I2C read (Length)
I2C read (Value #0)
I2C read (Value #n)
:
50msec time slot
50msec time slot
Must be less than 50msec

## Slide 7: Command from UART
Command queue
UART
Current slot
#0 | PLG
#1 | ADT
#2 | CMD
#3a | INV
#3b | SEN
#4a | INV
#4b | SEN
#5a | INV
#5b | SEN
#6a | INV
#6b | SEN
#7 | CMD
#8a | INV
#8b | SEN
#9a | INV
#9b | SEN
#10a | INV
#10b | SEN
#11a | INV
#11b | SEN

## Slide 8: Caveats
I2C communications limited to one byte data at each time  to be improved