## Slide 1: I2C backplane specification
https://github.com/araobp

## Slide 2: Specification
Master-slave I2C backplane
Max seven I2C slaves supported
Plug&play with I2C general call

## Slide 3: I2C backplane
Master
Slave
0x10
Slave
0x11
Slave
0x12
Slave
0x16
…
Max seven slaves
Vdd
3k ohm
3k ohm
Mini PLC
UART
I2C
Interval: 50msec * scaler
(default scaler value: 1)

## Slide 4: Scheduler and 50msec time slot
#0 | PLG
#1 | ADT
#2 | CMD
#3a | INV
#3b | SEN
#4a | INV
#4b | SEN
#5a | INV
#5b | SEN
#6a | INV
#6b | SEN
#7 | CMD
#8a | INV
#8b | SEN
#9a | INV
#9b | SEN
#10a | INV
#10b | SEN
#11a | INV
#11b | SEN
Slave 0x12
Slave 0x11
Slave 0x10
50 msec
PLG General call
Master
CMD
INV
SEN
INV
SEN
INV
SEN

## Slide 5: Slave with two MSSPs enabled
Slave
I2C write “INV”
Master
Another I2C device
I2C
MSSP2
(I2C master)
MSSP1
(I2C slave)
I2C write “SEN”
I2C read (Type)
I2C read (Length)
I2C read (Value #0)
I2C read (Value #n)
:
50msec time slot
50msec time slot
Must be less than 50msec

## Slide 6: Command from UART
Command queue
UART
Current slot
#0 | PLG
#1 | ADT
#2 | CMD
#3a | INV
#3b | SEN
#4a | INV
#4b | SEN
#5a | INV
#5b | SEN
#6a | INV
#6b | SEN
#7 | CMD
#8a | INV
#8b | SEN
#9a | INV
#9b | SEN
#10a | INV
#10b | SEN
#11a | INV
#11b | SEN

## Slide 7: Caveats
I2C communications limited to one byte data at each time  to be improved